## Slide 1
Company Network with VLANs and Inter-VLAN Routing

## Slide 5: Project Overview
Design a company network using VLANs
Implement Inter-VLAN Routing
Use GNS3 for simulation

## Slide 6: Objectives
Segment the network
Improve security
Reduce broadcast traffic
Enable communication between departments

## Slide 7: Network Topology
Two routers (Ramallah & Nablus)
Multiple switches
Several PCs
Departments separated logically

## Slide 8: What is VLAN
VLAN = Virtual Local Area Network
Divides one physical network into multiple logical networks
Each VLAN is isolated

## Slide 9: VLANs Used
VLAN 10 → HR
VLAN 20 → SALES
VLAN 30 → MANAGEMENT

## Slide 10: IP Addressing
HR → 192.168.10.0/24
SALES → 192.168.20.0/24
MANAGEMENT → 192.168.30.0/24

## Slide 11: Inter-VLAN Routing
Used Router-on-a-Stick
Created Subinterfaces
Each VLAN has its own gateway

## Slide 12: Trunking
Connects switches together
Carries multiple VLANs
Uses 802.1Q encapsulation

## Slide 13: Configuration Steps
Create VLANs
Assign switch ports
Configure trunk links
Setup router interfaces
Assign IPs to PCs

## Slide 14: Testing
Ping between devices
Test communication across VLANs
Verify routing

## Slide 15: Problems Faced
Native VLAN mismatch
Trunk encapsulation errors
Wrong IP configuration

## Slide 16: Solutions
Set same native VLAN
Use dot1Q encapsulation
Verify gateway addresses

## Slide 17: Conclusion
Network successfully segmented
VLANs implemented correctly
Inter-VLAN routing working